## Slide 1: Near Field Communication (NFC)
Protocols and weaknesses
INFO-F514 - Protocols, cryptanalysis and mathematical cryptology
27-03-2017
Arabella Brayer

## Slide 2: Content
Arabella Brayer
27-03-2017
Brief presentation
  Definition, purposes and requirements
  Several modes
  NFC : a set of protocols
A typical exchange with NFC
  Anti collision
  Mutual authentication
  One detailed example MIFARE Classic :
    PRNG initialization
    CRYPTO-1
Where is NFC today ?
  Some progress have been made :
    Opened protocols implemented
    External certifications
Discussion :
  Is the security sufficient now ? For what kind of use ?

## Slide 3: Brief presentation
Definition, purposes and requirements
  Field of RFID (Radio Frequency IDentification) : 13.56 MHz
  Not like a magnetic-stripe : CPU
  Another wireless connexion ?
    Rate of 106, 212, 428 of 848 kbit/s -> slow, low distance, …
Different modes for different use (Active / Passive)
  Read / Write (Tag and Reader) (P / A)
  Emulation (P / A)
  Peer-to-peer (A / A)
ISO/IEC 14443 1- 4 : Several layers (OSI model):
  Physical characteristics
  Radio frequency power and signal interface
  Initialization and anticollision
  Transmission protocol
Arabella Brayer
27-03-2017

## Slide 4: Brief presentation
Where is the security ?
Depends of the class tag.
  Class Tag :
ISO/IEC 14443A. read and re-write capable. Mem. 96 bytes - 2 kbyte
The same. Mem. 48 bytes - 2 kbytes
FeliCa. Mem. variable, theoretical mem. limit 1 MByte/service
Fully compatible ISO/IEC 14443A/B. Memory size can be up to 32 KBytes. For the communication with tags APDUs according to ISO 7816-4 (cryptographic applications) can be used.
  Emulation : Application level, secure element, etc.
  Peer-to-peer : NFC-SEC (see ECMA-385, 386)
Depends of device and utilization
Arabella Brayer
27-03-2017

## Slide 5: Anticollision
Arabella Brayer
27-03-2017
Following the ISO/IEC 14443, an anti collision protocol must start the transaction. In this way, information between Tag and Reader will be exchanged:
  Type of tag
  ID (UID and now RID)
  etc.
Afterward, the loop of anti collision can start.
...And then, the Authentication.

## Slide 6: Authentication (1)
Arabella Brayer
27-03-2017
How to authenticate ?
Using (usually) symmetric scheme, because low power
but… lower security too.
Authentication (ISO/IEC 9798):
Reader and Tag must share a secret key (k) before the process. Authentication is done by proving the possession of this secret key. For instance :
B choose a Random number (rB), send it to A
A sends the key k encrypted with rB : Ek(rB)
Then, B checks the result and the identity of A
How to process for the mutual authentication ?
Often use 3-pass mutual authentication
Notes: https://www.cs.virginia.edu/~kn5f/Mifare.Cryptanalysis.htm
décrire le 3 pass mutual authentication au tableau

## Slide 7: Authentication (2)
Arabella Brayer
27-03-2017
3-pass mutual authentication : challenge-response:
  Reader sends a Random Number (rA) to Tag
  Tag chooses a nonce (rB), encrypt rA and rB with k, and sends to Reader
  Reader can decode rA and rB, and can identify Tag. Changes the sequence, sends it back to the Tag, that can check its identity too.
A → B : rB
A ← B : Ek(rA, rB)
A → B : Ek(rB, rA)
Security mainly based on RGN and Encryption/Decryption function.
Has been implemented on the MIFARE Classic Tag (1994) with :
a PRGN (based on an Linear Feedback Shift Register (LFSR))
CRYPTO-1 (proprietary)
(publicly) Broken in 2007

## Slide 8: PRGN
Arabella Brayer
27-03-2017
Based on a LFSR
  The register is 32-bits long, but the feedback uses only 16 lower bits
    216 combinations
Additional problems with initialization found : always the same initial state, ...
WEAK !!
MIFARE Classic PRGN
Notes: demo of a LFSR computaion

## Slide 9: CRYPTO-1
Arabella Brayer
27-03-2017
Proprietary, known by reverse engineering (2007)
(Karsten Nohl, Henryk Plötz)
Consists of a LFSR and a function f(x)
Shift-register is first initialized with the secret key (48-bits)
PRGN products a 32-bits cipher that is XORed with the UID
Element passed in clear is used to initialize the register…
key of 48 bits, and weak PRNG, ...

## Slide 10: CRYPTO-1
Arabella Brayer
27-03-2017
A lot of known attacks (not exhaustive):
Brute Force because of the 48-bits size key, but off-line
Keystream recovery :
  Having a Reader and a (genuine) Tag
  Eavesdrop the communication
  Make sure that the card will use the same keystream
  Modify the plaintext
p1 ⊕ K = c1
p2 ⊕ K = c2
Because of the weak PRGN, is possible
Authentication replay
  Need a record of a successful authentication between tag and reader
  Send authentication request until get the same nonce that the recorded
  Send the recorded response …
Card-only
  ISO/IEC 14443 require parity bits after 8 bits. MIFARE classic uses plaintext combined with repeated keystream
…
C1 ⊕ C2 → P1 ⊕ P2 ⊕ K ⊕ K → P1 ⊕ P2

## Slide 11: Where is NFC today ?
Arabella Brayer
27-03-2017
Commercial product, so it depends of the device.
Some opened crypto-systems are implemented : DES, 3-DES, AES-128, directly on the chip. (MIFARE DESFire Family)
UID or RID
Authentication example with derived keys, and TRGN :
  Reader chooses a number, send it to Tag
  Tag derives the key according to this number, encrypt it with rB of 16 bytes
  Reader gets rB and chooses rA. rB’ computed by shifting left of 8 bits, then concatenates of rA and rB’, encrypts with AES-128 and send back
  The Tag decrypt, gets rB’, computes its own rB’ by the same way and compares with the received.
  … The same is done with rA
  The session key is : rA(0-3) + rB(0-3) + rA(12-15) + rB(12-15) (16 bytes)

## Slide 12: « NFC » well known attacks
Arabella Brayer
27-03-2017
Nowadays, constructors search to certificate their products. But compliance with the ISO/IEC 14443 does not answer at the known security possible attacks :
Eavesdropping
  Attacker uses an antenna to record the communication despite the short distance
  Can corrupt the information, making them useless
Relay attack
Privacy
Notes: http://proxmark.nl/files/Documents/13.56%20MHz%20-%20MIFARE%20DESFire/Cloning_Cryptographic_RFID_Cards_for_25USD-WISSEC_2010.pdf

## Slide 13: Is that enough for...
Arabella Brayer
27-03-2017
Building Access control, car access control, etc.
Payments
Transport tickets
Passport, identity cards…
?

## Slide 14
Thank you
Reference list :
1 - S. (2016). Analyse de sécurité des applications d’authentification par NFC (Unpublished master's thesis). Montreal. Retrieved February 26, 2017, from https://publications.polymtl.ca/2149/1/2016_SabrineJdaida.pdf
2 - K., M., G., I., & K. (2009, May 01). Attacking smart card systems: Theory and practice. Retrieved March 26, 2017, from http://www.sciencedirect.com/science/article/pii/S136341270900017X
3 - Chiu, Y., Hong, W., Chou, L., Ding, J., Yang, B., & Cheng, C. (2013, November 27). A Practical Attack on Patched MIFARE Classic. Retrieved March 26, 2017, from http://link.springer.com/chapter/10.1007/978-3-319-12087-4_10
4 - The MIFARE Hack (Master's thesis, Radboud University Nijmegen) (pp. 1-14). (2012). Mathias Morbitzer.
5 - K., D., S., & H. (2008). Reverse-Engineering a Cryptographic RFID Tag (Master's thesis, University of Virginia, Chaos Computer Club Berlin, 2008) (pp. 185-193). USENIX Association. Retrieved March 26, 2017, from https://www.usenix.org/legacy/event/sec08/tech/full_papers/nohl/nohl.pdf